## Slide 1: Unit-4
Network Layer

## Slide 2
Transmission Control Protocol (TCP):
TCP is a transport layer protocol for process-to-process communication like UDP. It is a connection oriented, reliable transport protocol. TCP creates a virtual connection between two TCP clients to send data. In addition, TCP uses flow and error control mechanisms at the transport level.
TCP Operations:
Various services and operations of TCP are as follows:
Process to Process Communication: Like UDP, TCP provides process-to-process communication using port numbers.
Stream Delivery Service: TCP is a stream-oriented protocol. It allows the sending process to deliver data as a stream of bytes and allows the receiving process to obtain data as a stream of bytes. TCP creates an environment in which the two processes seem to have a dedicated connection that carries their data across the internet. For flow control, TCP uses sending and receiving buffer that provides some storage for data packets in case of overflow. This prevents the loss of packets by synchronizing the flow rate.

## Slide 3
Full-Duplex Communication: TCP offers full-duplex services in which data can flow in both directions at the same time. Each TCP then has sending and receiving buffer, and segments move in both directions.
Connection-Oriented Service: When a process at site A wants to send and receive data from another process at site B, the following occurs:
• The two TCPs establish a connection between them.
• Data are exchanged in both directions.
• The connection is terminated.
Note that this a virtual connection, not a physical connection.
Reliable Service: TCP is a reliable transport protocol. It uses an acknowledgement mechanism to check the safe arrival of data. This is possible due to efficient error control mechanisms.

## Slide 4
Transmit Segments

## Slide 5
TCP Features and Characteristics:
To support the services of TCP, following are some features:
Numbering System: TCP keeps track of segments being transmitted or received. There are two fields called the sequence number and the acknowledgement number for numbering the bytes within the segments and acknowledgements respectively.
Flow control: TCP provides flow control mechanism. The receiver of the data controls the amount of data that are to be sent by the sender. This is done to prevent the receiver from being overloaded with data. The numbering system allows TCP to use a byte-oriented flow control.
Error Control: To provide reliable service, TCP implements an error control mechanism. Although error control mechanism considers a segment as the unit of data for error detection (loss or corrupted
segments), error control is byte-oriented.
Congestion Control: TCP takes into account about the congestion in the network. The amount of data sent by a sender is not only controlled by the receiver (flow control), but is also determined by the level of congestion in the network.

## Slide 6
TCP Segment structure –
A TCP segment consists of data bytes to be sent and a header that is added to the data by TCP as shown:

## Slide 7
The header of a TCP segment can range from 20-60 bytes. 40 bytes are for options. If there are no options, a header is 20 bytes else it can be of upmost 60 bytes.
Header fields:
Source Port Address – A 16-bit field that holds the port address of the application that is sending the data segment.
Destination Port Address – A 16-bit field that holds the port address of the application in the host that is receiving the data segment.
Sequence Number – A 32-bit field that holds the sequence number, i.e, the byte number of the first byte that is sent in that particular segment. It is used to reassemble the message at the receiving end of the segments that are received out of order.
Acknowledgement Number – A 32-bit field that holds the acknowledgement number, i.e, the byte number that the receiver expects to receive next. It is an acknowledgement for the previous bytes being received successfully.
Header Length (HLEN) –It specifies the length of the header which of 4 bit length.

## Slide 8
Control flags – These are 6 1-bit control bits that control connection establishment, connection termination, connection abortion, flow control, mode of transfer etc. Their function is:
URG: Urgent pointer is valid
ACK: Acknowledgement number is valid( used in case of cumulative acknowledgement)
PSH: Request for push
RST: Reset the connection
SYN: Synchronize sequence numbers
FIN: Terminate the connection
Window size – This field tells the window size of the sending TCP in bytes.
Checksum – This field holds the checksum for error control. It is mandatory in TCP as opposed to UDP.
Urgent pointer – This field (valid only if the URG control flag is set) is used to point to data that is urgently required that needs to reach the receiving process at the earliest. The value of this field is added to the sequence number to get the byte number of the last urgent byte.

## Slide 9
Three-Way Handshaking:
Since TCP is a connection-oriented service, it requires three phases: connection establishment, data
transfer, and connection termination.
The connection establishment in TCP is called three-way handshaking. The figure below shows the
handshaking process.
Similarly three way handshaking is also uesd for connection termination.

## Slide 10
User Datagram Protocol (UDP):
The user datagram protocol (UDP) is called a connectionless, unreliable transport protocol. It does not add anything to the services of IP except to provide process-to-process communication instead of hostto-host communication.
The UDP packet structure is as follows:

## Slide 11
Source Port: Source Port is a 2 Byte long field used to identify the port number of the source.
Destination Port: It is a 2 Byte long field, used to identify the port of the destined packet.
Length: Length is the length of UDP including the header and the data. It is a 16-bits field.
Checksum: Checksum is 2 Bytes long field. It is the 16-bit one’s complement of the one’s complement sum of the UDP header, the pseudo-header of information from the IP header, and the data, padded with zero octets at the end (if necessary) to make a multiple of two octets.

## Slide 12
Applications of UDP:
Used for simple request-response communication when the size of data is less and hence there is lesser concern about flow and error control.
It is a suitable protocol for multicasting as UDP supports packet switching.
UDP is used for some routing update protocols like RIP(Routing Information Protocol).
Normally used for real-time applications which can not tolerate uneven delays between sections of a received message.
UDP is widely used in online gaming, where low latency and high-speed communication is essential for a good gaming experience. Game servers often send small, frequent packets of data to clients, and UDP is well suited for this type of communication as it is fast and lightweight.
Streaming media applications, such as IPTV, online radio, and video conferencing, use UDP to transmit real-time audio and video data. The loss of some packets can be tolerated in these applications, as the data is continuously flowing and does not require retransmission.

## Slide 13
IPv4 Header Format:
20 - 65,535 bytes

## Slide 14
Version number. These 4 bits specify the IP protocol version of the datagram. By looking at the version number, the router can determine how to interpret the remainder of the IP datagram. Different versions of IP use different datagram formats.
HL(Internet Header Length - 4 bits): The minimum value is 5, and the maximum is 15. The header length is necessary because IPv4 allows for variable-length options.
Type of Service (8 bits): Originally intended for Quality of Service (QoS) settings, it includes the Precedence, Delay, Throughput, Reliability, and Cost of Service fields. However, these are not widely used, and the field is often set to zero.
Total Length (16 bits): Specifies the total length of the IPv4 packet (header + data). The maximum value is 65,535 bytes.

## Slide 15
Identification: If IP packet is fragmented during the transmission, all the fragmented contain same identification number to identify the original ip packet that belong too.
Flags: As required by the network resources, if ip packet is too large to handle,these flags tells if they can be fragmented or not.The first bit is reserved(not used).The second bit is called the do not fragment bit. If its value is 1, the machine must not fragment the datagram . If it cannot pass the datagram through any available physical network, it discards the datagram and sends an ICMP error message to the source host. If its value is 0, the datagram can be fragmented if necessary. The third bit is called the more fragment bit. If its value is 1, it means the datagram is not the last fragment . If its value is 0, it means this is the last or only fragment.

## Slide 16
Fragment offset: This offset tells the exact position of the fragment in the original Packet.
Time-to-live: Time-to-live. The time-to-live (TTL) field is included to ensure that datagrams do not circulate forever (due to, for example, a long-lived routing loop) in the network. This field is decremented by one each time the datagram is processed by a router. If the TTL field reaches 0, the datagram must be dropped.
Protocol. This field is used only when an IP datagram reaches its final destination. The value of this field indicates the specific transport-layer protocol to which the data portion of this IP datagram should be passed. For example, (e.g., TCP, UDP)
Header Checksum: This field is used to keep checksum value of entire header which is then used to check if the packet is received error-free.
Source address: This 32 bit field define the address of the sender.
Source address: This 32 bit field defines the address of the receiver.
Flag bits | 
1st bit | Reserved (not used)
2nd bit | Called do not fragment bit. -if value 1 = the datagram must not fragmented -If value 0 = the datagram can be fragmented
3rd bit | Called more fragment bit. -if value 1 = means the datagram is not last fragment If value 0 = means this is last fragment.

## Slide 17
Option:This is optional field , which is used if the value of IHL is greater than 5. this option may contain values for option such as security,record route,time stamp, etc.
Data(Payload): It is the last and important field. In most circumstances, the data field of the IP datagram contains the transport-layer segment (TCP and UDP) to be delivered to the destination. How ever the data can carry other type of data, such as ICMP message.
IPv4 issues: The major issues in IPv4 are
➢ Deficiency of address space - The devices connected to the Internet grows exponentially. The size of address space 2^32 is quickly exhausted;
➢ Too large routing tables

## Slide 18
IPv6 address: An Ipv6 made of 128 bits divided into eight 16 bits segment or block.
Ex: FDEC : BA98 : 0000 : 0000 : 0600 : BDFF : 0004 : FFFF
All IPv6 addresses are 128-bit hexadecimal addresses, written in 8 separate sections having each of them have 16 bits. As the IPv6 addresses are represented in a hexadecimal format, their sections range from 0 to FFFF. Each section is separated by colons (:). It also allows to removes the starting zeros (0) of each 16-bit section. If two or more consecutive sections 16-bit contains all zeros (0 : 0), they can be compressed using double colons (::).

## Slide 19
IPv6 addresses are consist of 8 different sections, each section has a 16-bit hexadecimal values separated by colon (:). IPv6 addresses are represented as following format:
xxxx : xxxx : xxxx : xxxx : xxxx : xxxx : xxxx : xxxx
Each "xxxx" group contains a 16-bit hexadecimal value, and each "x" is a 4-bit hexadecimal value. For example:
FDEC : BA98 : 0000 : 0000 : 0600 : BDFF : 0004 : FFFF
You can also remove the starting zeros (0) of each 16-bit section. For example, the above IPv6 can be rewritten by omitting starting zeros (0) as follow:
FDEC : BA98 : 0 : 0 : 600 : BDFF : 4 : FFFF
You can also compress the consecutive sections 16-bit zeros (0 : 0) using double colons (::). But keep in mind that you can do it only once per IP address.
FDEC : BA98 : : 600 : BDFF : 4 : FFFF

## Slide 20
Features of IPV6:
Larger address space: Approx 2^128.
Simplified Header: It is simplified by moving all unnecessary information and option to the end of the ipv6 header. Header size is 40 bytes.
End-to-end connectivity: no need of NAT
Auto Configuration: Ipv6 supports both stateful and stateless auto configuration mode of its host device.
Fast forwarding/Routing: simplified header puts all unnecessary information at the end of the header. Only important information is available at the front thus making routing decision is quickly.
Ipsec: Initially it was decided that IPV6 must have IpSec security, making it more secure than IPv4.This feature has now made optional.
Anycast:In this mode , multiple interface over the internet are assigned the same anycast Ip address. Router while routing send the packet to the nearest destination.
Mobility: Ipv6 was designed keeping mobility in mind. This feature enables hosts (such as mobile phone) to roam around in different geographical area and remain connected with same Ip address .

## Slide 21
IPV6 Datagaram Formats
Ipv6 has 4 times larger than IPV4, but the header of an ipv6 is only 2 times larger than that of ipv4.Ipv6 header have one fixed header and zero or more optional(extensoin) headers.All the necessary information that is essential for a router is kept in the fixed header.The extension header contains optional information that helps routers to understand how to handle a packet flow.
IPV6 Header | Extension Header | Upper Layer Protocol Data
Main information
Other optional infromation
Upper layer protocol(TCP,UDP,ICMP)

## Slide 23
Version (4-bits): It represents the version of Internet Protocol, i.e. 0110
Traffic Class (8-bits)(audio,video) These 8 bits are divided into two parts. The most significant 6 bits are used for Type of Service to let the Router know what services should be provided to this packet. The least significant 2 bits are used for Congestion Notification (ECN).
Flow Label (20-bits): This label is used to maintain the sequential flow of the packets belonging to a communication. The source labels the sequence to help the router identify that a particular packet belongs to a specific flow of information.
Payload Length (16-bits): This field is used to tell the routers how much information a particular packet contains in its payload. Payload is composed of Extension Headers and Upper Layer data.
Next Header (8-bits): This field identifies the protocol to which the contents of this datagram will be delivered for ex: TCP or UDP. This field uses the same values as the protocol field in the IPv4 header.
Hop Limit (8-bits): This field is used to stop packet to loop in the network infinitely. This is same as TTL in IPv4. The value of Hop Limit field is decremented by 1 as it passes a link (router/hop). When the field reaches 0, the packet is discarded.
Source Address (128-bits): This field indicates the address of originator of the packet.
Destination Address (128-bits): This field provides the address of intended recipient of the packet.

## Slide 24
IPv6 has three address categories:
Unicast - identifies exactly one interface
Multicast - identifies a group; packets get delivered to all members of the group
Anycast - identifies a group; packets normally get delivered to nearest member of the group

## Slide 25
Transition from IPv4 to IPv6:
Because of the huge number of systems on the internet, the transition from IPv4 to IPv6 cannot happen suddenly. The transition must be smooth to prevent any problems between IPv4 and IPv6 systems. Three strategies have been devised to help the transition:
Dual stack
Tunneling
Header translation
Dual Stack:
Dual-stack transition mechanism enables to run both IP stacks (IPv4 and IPv6) in a single node. Maintainsboth IP protocol stacks that operates parallel and thus allow the end node to use either protocols. Nodeis capable of handling both kinds of IP (IPv4&IPv6) routing. Flow or routing decisions in the node arebasedon IP header version’s field. Both IPv4 and IPv6 shares common transport layer protocols such as TCP/IP. Many of client and server operating systems provide dual IP protocol stacks. For example: Windows 7, 8, Linux

## Slide 26
The Dual Stack Router, can communicate with both the networks. It provides a medium for the hosts to access a server without changing their respective IP versions

## Slide 27
Tunneling:
Tunneling is a strategy used when two computers using IPv4 want to communicate with each other and the packet must pass through a region that uses IPv6. To pass through this region, the packet must have IPv6 address. So the IPv4 packet is encapsulated in an IPv6 packet when it enters the region, and it leaves its capsule when it exits the region. Seems as if the IPv4 packet goes through a tunnel at one end and emerges at the other end.

## Slide 29
Header Translation:
Translation mechanism refers the direct conversion of IP protocols. May include transformation of both IPv4 and IPv6 protocol’s header and payload according to their IP specifications. Translation mechanisms always need translators that can translate particular IPv4 address to particular IPv6 address and vice versa. A host with IPv4 address sends a request to an IPv6 enabled server on Internet that does not understandIPv4 address. In this scenario, the NAT-PT device can help them communicate. When the IPv4 host sends a request packet to the IPv6 server, the NAT-PT device/router strips down the IPv4 packet, removes IPv4header, and adds IPv6 header and passes it through the Internet. When a response from the IPv6servercomes for the IPv4 host, the router does vice versa.

## Slide 31
Routing:
Routing is a process that is performed by layer 3 (or network layer) devices in order to deliver the packet by choosing an optimal path from one network to another.

## Slide 32
1. Static Routing
Static routing is a process in which we have to manually add routes to the routing table.
Advantages
No routing overhead for the router CPU which means a cheaper router can be used to do routing.
It adds security because only an only administrator can allow routing to particular networks only.
No bandwidth usage between routers.
Disadvantage
For a large network, it is a hectic task for administrators to manually add each route for the network in the routing table on each router.
The administrator should have good knowledge of the topology. If a new administrator comes, then he has to manually add each route so he should have very good knowledge of the routes of the topology.

## Slide 33
Default Routing
Default Routing is a technique in which a router is configured to send all the packets to the same hop device, and it doesn't matter whether it belongs to a particular network or not. A Packet is transmitted to the device for which it is configured in default routing.
Default Routing is used when networks deal with the single exit point.
It is also useful when the bulk of transmission networks have to transmit the data to the same hop device.
When a specific route is mentioned in the routing table, the router will choose the specific route rather than the default route. The default route is chosen only when a specific route is not mentioned in the routing table.

## Slide 34
Dynamic Routing
It is also known as Adaptive Routing.
It is a technique in which a router adds a new route in the routing table for each packet in response to the changes in the condition or topology of the network.
Dynamic protocols are used to discover the new routes to reach the destination.
In Dynamic Routing, RIP and OSPF are the protocols used to discover the new routes.
If any route goes down, then the automatic adjustment will be made to reach the destination.

## Slide 35
The Dynamic protocol should have the following features:
All the routers must have the same dynamic routing protocol in order to exchange the routes.
If the router discovers any change in the condition or topology, then router broadcast this information to all other routers.
Advantages of Dynamic Routing:
It is easier to configure.
It is more effective in selecting the best route in response to the changes in the condition or topology.
Disadvantages of Dynamic Routing:
It is more expensive in terms of CPU and bandwidth usage.
It is less secure as compared to default and static routing.

## Slide 36
S.NO | Static Routing | Dynamic Routing
1. | In static routing routes are user-defined. | In dynamic routing, routes are updated according to the topology.
2. | Static routing does not use complex routing algorithms. | Dynamic routing uses complex routing algorithms.
3. | Static routing provides high or more security. | Dynamic routing provides less security.
4. | Static routing is manual. | Dynamic routing is automated.
5. | Static routing is implemented in small networks. | Dynamic routing is implemented in large networks.
6. | In static routing, additional resources are not required. | In dynamic routing, additional resources are required.

## Slide 37
7. | In static routing, failure of the link disrupts the rerouting. | In dynamic routing, failure of the link does not interrupt the rerouting.
8. | Less Bandwidth is required in Static Routing. | More Bandwidth is required in Dynamic Routing.
9. | Static Routing is difficult to configure. | Static Routing is easy to configure.
10. | Another name for static routing is non-adaptive routing. | Another name for dynamic routing is adaptive routing.

## Slide 38
Dynamic Routing Protocol
Interior Routing Protocol
Exterior Routing Protocol
Distance Vector Routing (RIP)
Bellmanford Algorithm
Link State Routing (OSPF)
Dijkastra’s Algorithm
Path Vector Routing (BGP)

## Slide 39
Link State Routing
Link state routing is a technique in which each router shares the knowledge of its neighborhood with every other router in the internetwork.
The three keys to understand the Link State Routing :
Knowledge about the neighborhood: Instead of sending its routing table, a router sends the information about its neighborhood only. A router broadcast its identities and cost of the directly attached links to other routers.
Flooding: Each router sends the information to every other router on the internetwork except its neighbors. This process is known as Flooding. Information sharing: A router sends the information to every other router only when the change occurs in the information.